| Voltage rating | AC220V 50/60Hz |
| --- | --- |
| Voltage limit | AC 180V~250V |
| Hysteresis | ≤2sec/day(25 ℃ ) |
| On/off operation | 45 On & 45 Off，22 times pulse |
| Power consumption | 5VA(max) |
| Dispaly | LCD |
| Minimum interval | 1 Minute(pulse/cycle 1 s) |
| Pulse | 1 Sec-59min 59 sec |
| Count down | 1 Sec-99 min 59 sec |
| Width | 2 Modules(36mm) |
| Installation Type | Din Rail |
| Power reserve | 3 Years (Lithium battery) |
| Switching contact | 1 Change over switch |
| Switching Contact at 250VAC, cosφ=1 | 16A |
| Switching capacity at 250VAC, cosφ=0.6 | 10A |
| Incandescent/HALogen lamp load | 2300W |
| Energy saving lamps | 22x7W, 18X11W, 16X15WM 16X20W, 14X23W |
| Service life | Mechancally | 107 |
|  | electrically | 105 |
| Ambient humidity | 35~85%rh |
| Ambient temperature | -10~+40 ℃ |
| Weight | approx150g |
| Certificate | CE EMC, CE LVD, Rohs |